## Slide 1: Can Capacity Markets ensure sufficient Investment in Power Generation? Evidence from US-American Independent System Operators
Máté Borvendég, Susanne Hantke
Technische Universität München
TUM School of Management
Center of Energy Markets
Munich, 21st June 2023

## Slide 2: Contents
Introduction
    1.1 Relevance for the Topic
    1.2 Research Question
    1.3 Methodology
Context and Data
Empirical Strategy
Results
Discussion
Conclusion
References

## Slide 3: 1. Introduction – Relevance for the Topic
How to ensure sufficient investment in generation capacity?
Regulate electricity prices (“energy only”).
Regulate the quantity and quality of generating capacity.
Two approaches:
Example Texas (ERCOT):
Market prices are best  energy-only concept
Missing money problem in energy-only markets
Price for electricity derived by operating costs (merit order)
Idea: Recover fixed costs during times when demand > supply (scarcity price)
Problem:
    Scarcity price too low due to price cap or
    Times with demand > supply do not occur sufficiently often/do not last long enough
    Potential lack of investment leads to blackouts
https://stoft.com/2021/02/frozen-electric-blackouts-intexas/
Winter storms in Texas (2011)

## Slide 4: 1. Introduction – Research Question
Evidence from US-American Independent System Operators
à Focus on NY ISO
From: Botterud, A., & Auer, H. (2020)
Can Capacity Markets ensure sufficient Investment in Power Generation?

## Slide 5: 1. Introduction – Methodology
Econometric model
  Dependent variable:
    Difference between generation capacity and demand:
  Independent variables:
    Capacity market prices
    Day-ahead electricity
    Wholesale fuel prices
    UCAP
                : installed capacity
                : price in capacity auctions
                : control variables
                : error term

## Slide 6: 2. Context and Data
New York Installed Capacity Market (ICAP)
Long Island
NYC
NYCA
G-J
From: NYISO Training Documents
Since the formation of the NY ISO in 1999
3 different kinds of auctions:
  Compulsory (spot)
  Optional (monthly, strip)
Installed capacity requirement:
  derived from load forecast
  adjusted by safety margin (IRM)
  tailored to the 4 localities

## Slide 7: 2. Context and Data
Installed Capacity Resources 2023: ca. 40 GW
Generation Capacity
Installed Capacity
Source: NPCC 2022 Interim New York Area Review of Resource Adequacy, NYISO, 2022; Preliminary Monthly Electric Generator Inventory (https://www.eia.gov/electricity/data/eia860M/)
Title with Python, smaller width
UCAP
Plot UCAP for all localities with Python
X-axis as daterange, don‘t tilt years

## Slide 8: 2. Context and Data
ICAP Capacity Prices
From: NYISO Market Prices, Custom Report for Day-Ahead Electricity Prices, NYISO, 2023 (https://www.nyiso.com)
Chart: NYISO ICAP Spot Auction Prices in $/MW-month
From: NYISO Market Prices, Custom Report for Day-Ahead Electricity Prices, NYISO, 2023 (https://www.nyiso.com)
Wholesale Electricity
Plot with Python
Put legend outside, on the right to the plot?

## Slide 9: 3. Empirical Strategy
Workflow
Basic model idea
Data collection
Separate model for each locality
Feature engi-neering

## Slide 10: 3. Empirical Strategy
Installed Capacities:
  Mapping to localities: electricity market zones ≈ counties  Assign power plants to zones  Aggregate zones to localities
  Upsampling (yearly  monthly) for data before 2017
Prices:
  Natural gas power plants build in approximately 2 years  Prices of today‘s auctions cannot influence today‘s capacity  Time lags of 2 to 4 years considered (account for planning period)
  Mapping to localities (mean)
  Downsampling (hourly  monthly)
Data Wrangling and Feature Engineering
Long Island
NYC
NYCA
G-J

## Slide 11: 3. Empirical Strategy
All parameters  multicollinearity
First Model

## Slide 12: 4. Results
Best Model or even all 4 models

## Slide 13: 4. Results
Model evaluation:
Statistically significant parameters:
  xy
Variance in “overinstalled“ capacity that can be described by the model:
Interpretation:
Reliability of supply ensured by

## Slide 14: 5. Discussion
Interpretation of results:
Differences in results in different localities
  Locality that is best described by capacity prices:
  Locality that is worst described by capacity prices:
??
Statistical problems:
Multicollinearity
Stationarity (time series)
Right time lags? (investors‘ hesitatement)
Omitted variables

## Slide 15: 6. Conclusion
Installed capacity is (not) driven by capacity prices
Main driver according to model is xy / Other drivers
However, in first years after installation of capacity markets (early 2000‘s), we see an increase in installed capacity
Security of supply is given
Oversupply  refer to paper

## Slide 16: 7. References
Data:
http://www.energyonline.com/Data/GenericData.aspx?DataId=13 (accessed on 14.06.2023)
http://www.energyonline.com/Data/GenericData.aspx?DataId=14&NYISO___ISO_Load_Forecast (accessed on 14.06.2023)
NY ISO exact links (latest access)
Literature:
https://stoft.com/2021/02/frozen-electric-blackouts-intexas/
See, P. C., Fosso, O. B., Wong, K. Y., & Molinas, M. (2015). Flow-based forward capacity mechanism: an alternative to the regulated capacity remuneration mechanisms in electricity market with high RES penetration. IEEE Transactions on Sustainable Energy, 7(2), 830-840.
Botterud, A., & Auer, H. (2020). Resource Adequacy with Increasing Shares of Wind and Solar Power: A Comparison of European and U.S. Electricity Market Designs. Economics of Energy and Environmental Policy, 9.
NYISO Training Documents: Installed Capacity (ICAP) Market, LSEs Capacity Obligations (https://www.nyiso.com/documents)

## Slide 17: Thank you for your attention!

## Slide 18: Back-up slides

## Slide 19: Safety-copy slides (duplicated versions)

## Slide 20: 1. Introduction – Relevance for the Topic
How to ensure sufficient investment in generation capacity?
Missing money problem in energy-only markets
Price for electricity derived by operating costs (merit order)
Idea: Recover fixed costs during times when demand > supply (scarcity price)
Problem:
    Scarcity price too low due to price cap or
    Times with demand > supply do not occur sufficiently often/do not last long enough
    Potential lack of investment leads to blackouts
https://stoft.com/2021/02/frozen-electric-blackouts-intexas/
Winter storms in Texas (2011)

## Slide 21: 1. Introduction – Relevance for the Topic
Missing Money Problem in Energy-only Markets
Price cap: A*
Price for electricity derived by operating costs (merit order)
Idea: Recover fixed costs during times when demand > supply (scarcity price)
Problem:
    Scarcity price too low due to price cap or
    Times with demand > supply do not occur sufficiently often/do not last long enough
From: See, P. C., Fosso, O. B., Wong, K. Y., & Molinas, M. (2015)